## Slide 1: A National Satellite-Based Forest Disturbance Detection System in Near-Real-Time Eastern Forest Environmental Threat Assessment Center USDA Forest Service, Southern Research Station, Asheville, NC
ForWarn Team
William W. Hargrove, PI (USDA-FS)
Steven P. Norman (USDA-FS)
William M. Christie (USDA-FS)
Joseph P. Spruce (CSC, NASA Stennis)
Partners
USGS EROS Data Center, SD
CSC-NASA Stennis Space Center, MS
DOE Oak Ridge National Laboratory, TN
UNC-Asheville, NC: NEMAC

## Slide 2
What is ForWarn and How does it Work?
The Forest Change Assessment Viewer
Disturbance Assessment and Vetting
The ForWarn Website: http://forwarn.forestthreats.org
What’s New and Future Enhancements
Points of Contact
Questions?

## Slide 3
A national-scale near real-time satellite-based recognition and tracking system for all land cover disturbances
"Officially" rolled-out in 2012, but has actually been operating since January 2010
ForWarn covers the entire lower 48 United States
Generates new potential disturbance maps every 8 days, even throughout the winter
  Detects most types of regional and local land cover disturbances
    insects, diseases, wildfires, ice and frost damage, tornadoes, hurricanes, blowdowns, harvest, urbanization, seasonal timing and drought. and landslides
231 meter native resolution map cells (13-acre minimum mapping unit)
  It is not necessary for an entire forested pixel to be disturbed for disturbance to be detected

## Slide 4
In 2011, airborne observers from the Aerial Disturbance Survey (ADS) program covered about 70% of forests within the lower 48 United States once with visual observations from light aircraft
The ForWarn System covers essentially 100% of the forests within the lower 48 United States every 8 days
The two tiers are complementary:
  ForWarn is coarse-scaled, automated and extensive, and has a very high repeat rate
  Aerial surveys are finer-scaled, but require experienced observers, are labor-intensive and expensive, are a safety risk, are limited in extent and are completed once-a-year
The two different systems can support each other well
tactical
strategic

## Slide 5
Based on a simple comparison between current greenness vs. historical greenness
We develop this historical greenness from the 16-year historical MODIS satellite record
The comparison is both spatially and temporally explicit – compares during the same 24-day period and for the same MODIS pixel
If the current NDVI value is less than 100% of the baseline used = Potential Disturbances
  shown as Greens, Yellows, and Reds
If the current NDVI value is greater than 100% of baseline greenness = Vegetation Regrowth or Recovery
  shown as Blues
Only shows a Disturbance if it affects the plants - and to the degree that it affects the plants
When first opening the ‘Forest Change Assessment Viewer’, only forested areas are shown by default, but ForWarn detects disturbances in all NLCD-based land use and land cover classes, including agricultural crops and rangeland forage (see the new “Masking” tool)
How Does ForWarn Work?

## Slide 6
ForWarn produces seven types of disturbance maps every 8 days, each emphasizing the age of disturbances that are displayed
1
2
3
4

## Slide 7
ForWarn produces seven types of disturbance maps every 8 days, each emphasizing the age of disturbances that are displayed
Most often used
1
2
3
4

## Slide 8
ForWarn produces seven types of disturbance maps every 8 days, each emphasizing the age of disturbances that are displayed
http://forwarn.forestthreats.org/products/near-real-time
5
6
7

## Slide 9
ForWarn produces seven types of disturbance maps every 8 days, each emphasizing the age of disturbances that are displayed
http://forwarn.forestthreats.org/products/near-real-time
These long-term baseline products also contain ‘fresh’ departures. The calculation method employed for these two, differ from the other change products and can offer additional discriminatory power when attempting to vet cause
5
6
7

## Slide 10
ForWarn 1 year baseline vs. All-year baseline

## Slide 11
ForWarn 1 year baseline vs. All-year baseline

## Slide 12
Relative to a 1-year baseline, forest vegetation is re-growing within the Yazoo, MS tornado track. ForWarn can easily track such recovery, and the rate of recovery is highly variable.
Positive NDVI Departure = Vegetative Recovery / Re-Growth

## Slide 13
ForWarn 1yr Baseline ‘Standard’ Product vs. 1yr Baseline ‘Early Detect’ Product
The ‘Early Detect’ product dramatically reduces ForWarn detection speeds, allowing the detection of disturbances in as few as one 8-day period

## Slide 14
Forest Change Assessment Viewer (FCAV)

## Slide 15
Forest Change Assessment Viewer (FCAV): Default View = Current 1yr BL with Forest Mask

## Slide 16
Forest Change Assessment Viewer (FCAV): Current 1yr BL, ‘All-Lands’ (no mask)
*
* Herbaceous wetlands only, woody wetlands were are placed in the Deciduous Forest class

## Slide 17
FCAV Feature: Graph NDVI (110B NDVI observations)

## Slide 18
FCAV Feature: Graph NDVI (use zoomed with transparency to guide pixel selection)

## Slide 19
FCAV Feature: “Share this Map”(share your area of concern with your colleagues)
Share this Map
Users can cut, paste and send a URL that, when clicked on by others, launches the Assessment Viewer showing them exactly the same ForWarn disturbance map being viewed by the sender.
Same map composition and extent
Facilitates communication and consultation with the ForWarn Team and your colleagues

## Slide 20
Forest Change Assessment Viewer (FCAV): Map Layers Window

## Slide 21
Forest Change Assessment Viewer (FCAV) Layers: Boundaries

## Slide 22
Forest Change Assessment Viewer (FCAV) Layers: Fire

## Slide 23
Forest Change Assessment Viewer (FCAV) Layers: ADS, PEST PROXIMITY
Pest Proximity Feature
Pest Proximity shows a list of all of the "Usual Suspects" -- all insects and diseases that have been found by the Aerial Disturbance Survey program -- near any point where the user clicks with the mouse
Shown in order of greatest likelihood, by area affected
‘Pest-Prox’ is designed to help you think of all of the likely possible causative disturbance agents

## Slide 24
Google Trends Pest-Prox Feature
Clicking on a Pest in Pest-Prox list does a Google Trends search, shows how frequently people have done a Google search on that Pest since 2004 – May, show:
historical seasonality of attack, and
relative magnitude / importance/interest of the attack this year, via indirect use of "Citizen Science.“
interesting feature, though all of you are the experts
FCAV Layer PEST-PROX, Google Trends: Social ”Crowd-Sourcing”

## Slide 25
FCAV Layers: Near-Real-Time Change Maps

## Slide 26
FCAV Layers: Cloud Assessment Maps (available from 01/08/06 through 09/29/15)

## Slide 27
FCAV Layers: Cloud Assessment Maps (available from 01/08/06 through 09/29/15)

## Slide 28
FCAV Layers: Cloud Assessment Maps (available from 01/08/06 through 09/29/15)

## Slide 29
Forest Change Assessment Viewer (FCAV) Layers: Drought Monitor Maps

## Slide 30
Forest Change Assessment Viewer (FCAV) Layers: Weather and Climate

## Slide 31
Forest Change Assessment Viewer (FCAV) Layers: Additional Assessment Maps

## Slide 32
Forest Change Assessment Viewer (FCAV) Layers: Additional Assessment Maps
50 Distinct Phenological Classes

## Slide 33
FCAV Layers: Additional Assessment Maps – Phenological Ecoregions
Annual Greenness Profile Through Time

## Slide 34
FCAV Layers: Additional Assessment Maps – Phenological Ecoregions
The 50 Most-Different National Phenological Ecoregions for 2010, Colored Randomly. This map is essentially a Dynamically Determined Vegetation Types Map.
50 Distinct Phenological Classes
Provisional Research Dataset

## Slide 35
ForWarn: Disturbance Assessment and Vetting

## Slide 36: Examples of forest disturbance, or recovery, seen in the ForWarn forest change images

## Slide 37: ForWarn Forest Disturbance Assessment (locate, characterize and assess)
Where is the Disturbance Located? (geographic site and situation)
  Land cover / Land Use (image basemap, NLCD masks, FS/GAP veg maps)
  Topographic position (elevation, slope and aspect, USGS topo's are available in Viewer under ‘Base maps’, wet/dry – USGS Stream Gauges, amount of mix?)
What is the character of the NDVI departure?
  Progression speed (use the 3 most recent, fast vs. slow, on in 1/off in next = clouds)
  Severity, percent NDVI change (pos./neg., low/high departure, climate affects?)
  Spatial extent (large area or localized)
  Pattern and shape (spotty/scattered, bulls-eye, target-like, linearity)
  Edges (hard/well defined or bulls-eye – trails-off showing less departure)
  Seasonality (spring, fall, snow: local and regional variation in annual phenology can causes NDVI departure (+/-); two new forest change products attempt to mitigate the effects in the variability of the start and stop of spring and fall from year to year)

## Slide 38: Examples of forest disturbance, or recovery, seen in the ForWarn forest change images

## Slide 39: Examples of forest disturbance, or recovery, seen in the ForWarn forest change images

## Slide 40: Examples of forest disturbance, or recovery, seen in the ForWarn forest change images

## Slide 41: Examples of forest disturbance, or recovery, seen in the ForWarn forest change images
Monongahela National Forest, Pocahontas County, WV and
George Washington National Forest, Highland County, VA

## Slide 42: Examples of forest disturbance, or recovery, seen in the ForWarn forest change images
ForWarn 07/27/2015, 1-year baseline

## Slide 43: Examples of forest disturbance, or recovery, seen in the ForWarn forest change images
Landsat 7, 07/22/2015, 452rgb

## Slide 44: Examples of forest disturbance, or recovery, seen in the ForWarn forest change images

## Slide 45: Examples of forest disturbance, or recovery, seen in the ForWarn forest change images

## Slide 46: Examples of forest disturbance, or recovery, seen in the ForWarn forest change images

## Slide 47: Examples of forest disturbance, or recovery, seen in the ForWarn forest change images

## Slide 48: Examples of forest disturbance, or recovery, seen in the ForWarn forest change images
Forest disturbance events often display degrees of severity. Variation in rates of recovery can relate to ecological, or vegetative resilience.

## Slide 49: Examples of forest disturbance, or recovery, seen in the ForWarn forest change images

## Slide 50: Examples of forest disturbance, or recovery, seen in the ForWarn forest change images

## Slide 51: Examples of forest disturbance, or recovery, seen in the ForWarn forest change images

## Slide 52
FCAV Feature: Graph NDVI (110B NDVI observations)

## Slide 53
FCAV Feature: Graph NDVI (110B NDVI observations)

## Slide 54
FCAV Feature: Graph NDVI (110B NDVI observations)

## Slide 55
FCAV Feature: Graph NDVI (control the x and y axis)

## Slide 56
forwarn.forestthreats.org
ForWarn Website

## Slide 57
ForWarn Website: Highlights

## Slide 58
If you need a quick shapefile of a specific disturbance event, you can use the WMS on the desktop to screen-digitize the extent, and if present, depict zones of severity.
ForWarn Website: Products

## Slide 59
(independent from the USFS)
ForWarn WMS on Android Devices

## Slide 60
ForWarn Website: Resources

## Slide 61
ForWarn Website: User’s Guide

## Slide 62
ForWarn Viewer: User’s Guide / Product Information

## Slide 63
What is ForWarn and How does it Work?
The Forest Change Assessment Viewer
Disturbance Assessment and Vetting
The ForWarn Website: http://forwarn.forestthreats.org
What’s New and Future Enhancements
Points of Contact
Questions?

## Slide 64
ForWarn FCAV: What’s New
New Land Cover Masks
MODIS Resolution 2010 Land Cover from NLCD
(from cec.org and landsat.usgs.gov)
*
(*) Hybridized – Woody wetland component of the Wetland class has been merged with the Deciduous Forest class
Benefit: Better overall representation and more accurate delineation of the “Mixed Forest” class

## Slide 65
‘Urbanness’ Data Layers
Population density Index modeled using LandScan and NLCD Impervious Surfaces
Benefit: Can be used to locate and monitor the WUI for wildfire potential, fuel treatment, harvests, controlled burns and smoke management. These data were produced in a uniform manner for CONUS.
ForWarn FCAV: What’s New

## Slide 66
Federal Lands Boundary
Proclaimed vs. Administered
ForWarn FCAV: What’s New

## Slide 67
Federal Land Boundaries’ Data Layer
Proclaimed vs. Administered
Holly Springs National Forest
Benefit: Proclaimed boundaries are misleading, view detailed parcel ownership when zoomed
ForWarn FCAV: What’s New

## Slide 68
ForWarn FCAV: What’s New
MODIS NDVI Data Distribution Site
Oak Ridge National Laboratory, Oak Ridge, TN
Benefit: Internet access to ForWarn’s NDVI-value data

## Slide 69
ForWarn FCAV: What’s New
Intra-Annual ‘Persistence’ Product
In development, a value-added product to aid users
NDVI Polar Graph
Benefit: Reduce disturbance complexity in the annual products and summarize persistent forest disturbance over a short period of time

## Slide 70
ForWarn FCAV: What’s New
Intra-Annual ‘Persistence’ Product
In development, a value-added product to aid users
NDVI Polar Graph
Benefit: Reduce disturbance complexity in the annual products and summarize persistent forest disturbance over a short period of time

## Slide 71
ForWarn General Technical Report (USFS GTR)
http://www.srs.fs.fed.us/pubs/gtr/gtr_srs180.pdf
Google ‘forwarn gtr’, first listing
(paper copies are also available)

## Slide 72: For More Information
ForWarn Website: http://forwarn.forestthreats.org
Forest Change Assessment Viewer: http://forwarn.forestthreats.org/fcav2
Bill Hargrove (PI), Research Ecologist: whargrove@fs.fed.us Steve Norman, Research Ecologist: stevenorman@fs.fed.us Bill Christie, Biological Scientist: wchristie@fs.fed.us
Many persons at many agencies have contributed to this work

## Slide 73
What is ForWarn and How does it Work?
The Forest Change Assessment Viewer
Disturbance Assessment and Vetting
The ForWarn Website: http://forwarn.forestthreats.org
What’s New and Future Enhancements
Points of Contact
Questions?

## Slide 74
Questions?
forwarn.forestthreats.org
Bill Hargrove, PI
Research Ecologist